## Slide 1: A Brief Introduction to Architectural Modeling Using AADL and Collaborative, Adaptive Cruise Control
John D. McGregor
Roselane S. Silva

## Slide 2: Origins
The Architecture Analysis and Design Language (AADL) is an architecture description language that is a standard from the Society of Automotive Engineers (SAE)
The Open Source AADL Tool Environment (OSATE) has been developed by the Software Engineering Institute (SEI) of Carnegie Mellon University. OSATE is an Eclipse-based open source IDE for architecture analysis and design.

## Slide 3: OSATE Installation
The latest version of OSATE can be downloaded from
http://www.aadl.info/aadl/osate/stable
You must have Java 8 installed on your machine
Example projects can be found at https://github.com/osate/examples

## Slide 4: Collaborative, Adaptive Cruise Control (CACC)
We will use examples from an architecture description for a family of cruise control devices.
A CACC maintains a fixed distance from a vehicle in front of you.
An ACC maintains a speed using accelerator and brakes.
A CC keeps the vehicle at least at the set speed but may go faster if going downhill.

## Slide 5: Structuring the description
We will use 4 perspectives in creating a complete architecture model
  Functional architecture
  Conceptual architecture
  Design architecture
  Integration architecture

## Slide 6: Keep descriptions modular
In the Navigator in OSATE you can see the .aadl files that divide the description

## Slide 7: AADL Component categories
System, abstract are composite structures that are hardware/software independent
Process, thread, subprogram are software specific types of structures
Device, processor, memory, bus are hardware specific types of structures

## Slide 8: Specification/Implementation
A specification describes what the component does but not how it does it.
The implementation describes how the component achieves the “what”.
Specifications have a user-created name
    Such as “sensor” or “brake”
Implementations are named by:
specification name.madeupName
sensor.impl or brake.boschModel12

## Slide 9: Basic structure of a component specification
system read_sensor
  Features
  …
  Flows
  …
  Properties
  …
end read_sensor;
Each structure can be thought of as a module or “container”
Each feature is information moving into or out of the container
Each flow is a sequence of computations involving multiple modules
A property is a non-functional attribute

## Slide 10: Input and Output
Each component specifies a set of ports
The name given a port should be descriptive
Each port has a direction in, out , or inout
Each port has either data, events, or event data flowing through .
Eventually each port should specify the type of information passing through but in the initial stages the type is often omitted until the system is better understood.

## Slide 11: system
A system can be thought of as an encapsulated black box that may represent a complete product or some complete subset
A system may represent some concept that we cannot yet decide whether it will be represented by hardware or software in the final system
For example, any physical entity or concept may be represented as a system.

## Slide 12: sensor
system sensor
  features
    sense: in data port;
    report out data port;
  flows
  computation_path0 : flow path sense -> report;
  Properties
  Latency=> 3ms..5ms applies to report;
end sensor; --every specification has an end
The in port receives data from a hardware sensor
The out port provides the current data held by the sensor
Where the data is stored inside sensor is not defined
The latency (how long it takes) budget for report is given

## Slide 13: Functional architecture
This architecture defines what the system will do.

## Slide 14: For the standard cruise control - cc
system cc
features
target_speed: in data port;
directed_action: out event data port;
sensor_data: in port;
end cc

## Slide 15: Adaptive cruise control
system acc extends cc
features
target_front_gap: in data port;
end acc;

## Slide 16: Collaborative adaptive cc
system cacc extends acc
features
target_rear_gap: in data port;
end cacc;

## Slide 17: Data type
data gps
end gps;
data implementation gps.impl
subcomponents
    speed: data speed;
    distance: data distance;
    location: data location;
end gps.impl;

## Slide 18: Adding data types
system cc
features
target_speed: in data port;
directed_action: out event data port;
sensor_data: in port gps;
end cc

## Slide 19: Conceptual architecture
This architecture will describe the hardware and software environment.

## Slide 20: Collaborative, Adaptive Cruise Control (CACC) - 2
Driver
Set/Coast
Resume/Accelerate
Cancel
ECU
Set gap
actuator
throttle
brake
Speed sensor
accelerometer
feedback
vehicleSensor

## Slide 21: Collaborative, Adaptive Cruise Control (CACC) - 3
Driver
Set/Coast
Resume/Accelerate
Cancel
ECU
Set gap
actuator
throttle
brake
Speed sensor
accelerometer
feedback
vehicleSensors
Sensor fusion
cloud
HERE interface
DSRC radio
J2735 messages

## Slide 22: An operating system
Like Windows defines a set of processes that divide the logical namespace
Each process defines one or more sequences of instructions to be carried out. These are termed threads.
The instructions are divided into subprograms

## Slide 23: Engine control unit
The “cpu” in a vehicle is referred to as an engine control unit (ecu) and it often has multiple processors
The memory associated with the ECU is connected via a bus – read only memory (ROM) and random access memory (RAM)
Other devices are also connected to the ecu via multiple types of bus

## Slide 24: Specification of bus access
device cameraSensor_rt extends sensor::generic_sensor
features
  sensor_data_out: refined to out data port data_types::picture;
  BA: requires bus access platform::generic_bus;
  Provides bus access
  bus_gps: bus access this_bus<->gps.BA;

## Slide 25: Binding
Binding of a thread to the hardware
--possible binding
Allowed_Processor_Binding => (reference(this_processor)) applies to vehicle_controller.thread_camera;
--concrete binding
Actual_Processor_Binding => (reference(this_processor)) applies to vehicle_controller.thread_gps;

## Slide 27: Design architecture
This architecture drills down to processes and threads within each module.

## Slide 28: Each structure …
Within each system we design an implementation for satisfying the specification
Divide the implementation into a disjointed set of data and computations each in its own operating system process
Within each process computations that are independent of each other are defined as threads

## Slide 29: process
A process defines a protected set of memory where data of the process is stored
The process protects that memory from access by other processes
An AADL process has same basic structure as other structures
Property definitions can

## Slide 30: thread
A thread is a sequence of computations.
All threads have access to the data defined within the process that contains the thread
The thread also has the address of a memory location that is the current executing instruction

## Slide 31: Controller process specification
process control_rt extends controller::generic_controller
features
  sensor1_data_in: refined to in data port data_types::radar_info;
  sensor2_data_in: refined to in data port data_types::picture;
  sensor3_data_in: refined to in data port data_types::gps;
  sensor4_data_in: refined to in data port data_types::speed;
  brake_failed: refined to in event data port;
annex EMV2 {**
  use types error_library;
  use behavior error_library::stateMachine;
**};
end control_rt;

## Slide 32: Process implementation
process implementation control_rt.impl extends controller::generic_controller.threads
subcomponents
  thread_radar: refined to thread read_radar.impl {Classifier_Substitution_Rule => Type_Extension;}; -- in modes (acc,cacc, cc, failure);
  thread_camera: refined to thread read_camera.impl {Classifier_Substitution_Rule => Type_Extension;};
  thread_gps: refined to thread read_gps.impl {Classifier_Substitution_Rule => Type_Extension;};
  thread_speedometer: refined to thread read_speedometer.impl {Classifier_Substitution_Rule => Type_Extension;};
  thread_controller: refined to thread thread_controller.impl;
  control_modal: refined to thread control_modal.impl {Classifier_Substitution_Rule => Type_Extension;};

## Slide 33: Connections among threads
connections
-- connect process w/ threads A,B,C
radar_thread_conn: port sensor1_data_in->thread_radar.sensor_in;
camera_thread_conn: port sensor2_data_in->thread_camera.sensor_in;
gps_thread_conn: port sensor3_data_in->thread_gps.sensor_in;
speedometer_thread_conn: port sensor4_data_in->thread_speedometer.sensor_in;
-- connect threads A,B,C w/ thread D
radar_controller_conn:port thread_radar.sensor_out->thread_controller.data_in;
camera_controller_conn:port thread_camera.sensor_out->thread_controller.data_in;
gps_controller_conn:port thread_gps.sensor_out->thread_controller.data_in;
speedometer_controller_conn:port thread_speedometer.sensor_out->thread_controller.data_in;
-- connect thread C w/ thread D
threads_conn: port thread_controller.data_out->control_modal.sensor_data;
-- connect UI w/ thread E (control_modal)
UI_conn:feature group UI_inverse_ports -> control_modal.UI_ports;

## Slide 34: Flows through a component
modal_proc_conn:port control_modal.feedback->feedback;
preferences_conn:port preferences.speed_limit-> control_modal.speed_limit;
-- connect modal w/ process
modal_coon: port control_modal.cmd -> current_speed;
brake_conn:port brake_failed->control_modal.brake_failed;
flows
UI_sink : flow sink UI_inverse_ports -> UI_conn -> control_modal.UI_sink;
controller_path0a : flow path sensor1_data_in -> radar_thread_conn -> thread_radar.thread_path0 -> radar_controller_conn
-> thread_controller.controller_thread_path0 -> threads_conn -> control_modal.control_modal_path0 ->modal_coon -> current_speed;

## Slide 35: System modes
modes
manual: initial mode;
cc: mode;
acc: mode;
cacc: mode;
failure: mode;
-- turn on/off
manual -[UI_inverse_ports.turn_on_off]-> cc;
-- cc
cc -[UI_inverse_ports.set_speed_down]-> cc;
cc -[UI_inverse_ports.turn_on_off]-> manual;
cc -[UI_inverse_ports.set_speed_up]-> cc;
cc -[UI_inverse_ports.set_speed_down]-> manual;
cc -[brake_failed]-> failure;

## Slide 36: Thread
thread read_gps extends controller::read_sensor
features
sensor_in: refined to in data port data_types::gps;
end read_gps;
thread implementation read_gps.impl
end read_gps.impl;

## Slide 37: Error library
package error_library
public
annex EMV2 {**
error types
NoPower : type;
ValueError: type;
NoValue: type extends ValueError;
InvalidValue: type extends ValueError;
BadValue: type extends ValueError;
TimingError: type;
EarlyValue: type extends TimingError;
LateValue: type extends TimingError;
ServiceError : type;
HardwareFailure: type;
SoftwareFailure: type;
end types;

## Slide 38: Error library - 2
error behavior stateMachine
states
  Operational : initial state;
  Failed : state;
end behavior;
**};
end CACC_model::error_library;

## Slide 39: Property set
MIPSCapacity: aadlreal units SEI::Processor_Speed_Units applies to (processor, system);
MIPSBudget: aadlreal units SEI::Processor_Speed_Units applies to (thread, thread group, process, system, device, virtual processor);
RAMCapacity: aadlreal units Size_Units applies to (memory, system);
RAMBudget: aadlreal units Size_Units applies to (thread, thread group, process, system, device);
ROMCapacity: aadlreal units Size_Units applies to (memory, system);
ROMBudget: aadlreal units Size_Units applies to (thread, thread group, process, system, device);
PowerCapacity: aadlreal units SEI::Power_Units applies to (bus, system, device, abstract);
PowerBudget: aadlreal units SEI::Power_Units applies to ( feature);
PowerSupply: aadlreal units SEI::Power_Units applies to ( feature);
BandWidthCapacity: aadlreal units Data_Rate_Units applies to (bus, system);

## Slide 40: Capturing hazard analysis
properties
emv2::hazards =>
([failure => "InvalidValue";
description => "Invalid data from the camera";
comment => "Would impact the detection of obstacle if the camera is not working as well";
])
applies to sensor_data_out.novalue;

## Slide 41: Integration architecture
The integration architecture uses specific modules and implementation to weave together the complete product.

## Slide 43: Top level
system cacc_rt extends abstracts::cacc
end cacc_rt;
The top system has no features. It is a self-contained system.

## Slide 44: System implementation-1
system implementation cacc_rt.devices extends abstracts::cacc.devices
subcomponents
vehicle_controller: refined to process control_rt.impl {Classifier_Substitution_Rule => Type_Extension;};
interface_controller:refined to process interface_controller_rt.impl;
radar_sensor: refined to device radarSensor_rt.impl {Classifier_Substitution_Rule => Type_Extension;};
radar_handler:refined to system radar_handler.impl;
camera_sensor:refined to device cameraSensor_rt.impl {Classifier_Substitution_Rule => Type_Extension;};
camera_handler:refined to system camera_handler.impl;
speedometer: refined to device speedometer_rt.impl {Classifier_Substitution_Rule => Type_Extension;};
speedometer_handler:refined to system speedometer_handler.impl;

## Slide 45: System implementation-2
Connecting bus to those that need bus
bus_processor:bus access this_bus<->this_processor.net;
bus_memory:bus access this_bus<->this_memory.BA;
Connecting ports
brake_cont_conn:port brake_actuator.brake_failed->vehicle_controller.brake_failed;
controller_driverSelection: port vehicle_controller.driverSelection -> states.driverSelection;

## Slide 46: Explicit Bindings
properties
-- bound thread to the processor
Actual_Processor_Binding => (reference(this_processor)) applies to vehicle_controller.thread_radar;

## Slide 47: Error states based on multiple components
composite error behavior
states
[radar_handler.Failed and camera_handler.Failed and gps_handler.Failed and speedometer_handler.Failed]-> Failed;
[radar_handler.Failed and camera_handler.Failed]-> Failed;

## Slide 48: Parking lot

## Slide 49: Resolute – verification tool
bound(logical : aadl, physical : component) : bool =
memory_bound(logical, physical) or
connection_bound(logical, physical) or
processor_bound(logical, physical)
memory_bound(logical : aadl, physical : component) : bool =
has_property(logical, Deployment_Properties::Actual_Memory_Binding) and
member(physical, property(logical, Deployment_Properties::Actual_Memory_Binding))