## Slide 1: CPSC 875
John D. McGregor
Quality Attribute Design

## Slide 2
We have identified 2 major structures in the wireless charging architecture.
We skipped over the QA reasons for these structures so I want to revisit those decisions.

## Slide 3: 2 major elements
Feedback control loop
Dynamic service discovery

## Slide 4: QA priorities for wireless charging
Safety
Availability
Efficient (performance)
Flexibility
Modifiable
Security

## Slide 5: Major risk
Overheating of the coil is a major risk to safety.
If not regulated there is a high probability of overheating.
If it overheats, the consequences are a fire which destroys the vehicle.
We can’t reduce the fire risk so we try to reduce the probability by controlling the flow of electricity.

## Slide 6: Feedback Control loop
The feedback control loop style monitors the flow of electricity and can keep it within range.
This style reduces the probability of overheating.
Must be able to adjust System faster than the System can change its output
Control
System
Monitor

## Slide 7: Service Oriented
The service oriented style provides flexibility due to the ease with which a new service can replace an existing one.
However, dynamic discovery is too error prone for a real-time system.
This is a safety concern and an availability concern.
Use SOA but not dynamic discovery; have a local registry

## Slide 8: What’s next
Security