## Slide 1: CPSC 875
John D. McGregor
Security

## Slide 2
Write down the AADL specification for a simple queue

## Slide 3: Microsoft’s Definition
Security is the capability of a system to prevent malicious or accidental actions outside of the designed usage, and to prevent disclosure or loss of information. A secure system aims to protect assets and prevent unauthorized modification of information.

## Slide 4: Security decomposes to
Confidentiality
Integrity
Availability
Reliability
Maintainability

## Slide 5: QA scenario - Integrity
Source of stimulus – would-be hacker
Stimulus – rapid sequence of DSRC messages
Environment – car is idling in parking lot
Artifacts – meta-data logging system activity
Response – message queue overflows but control is passed to a routine that resets the queue
Response measure – car did not change state

## Slide 6: QA scenario - Confidentiality
Source of stimulus – would-be hacker
Stimulus – unexpected Bluetooth message attempting to load phone contacts list
Environment – car is moving; Bluetooth is active
Artifacts – phone contacts list in txt format
Response – the system checks for authentication code and does not find it
Response measure – all unauthorized contacts are rejected

## Slide 7: QA scenario - Availability
Source of stimulus – would-be hacker
Stimulus – repeated door lock messages
Environment – car is parked in parking lot
Artifacts – door lock queue on the same bus as the engine controls
Response – message queue overflows but control is passed to a routine that refuses to respond to requests for a period of time
Response measure – system processes all authorized messages on time

## Slide 8: Intrusion points

## Slide 9: Vehicle networks

## Slide 10: Some things to do
Understand the potential threats for your domain
Reduce the attack surface
Set explicit policies such as access rights
Build complete system specification
  Use flows to identify unusual use of system
  Design responses to identified intrusions

## Slide 11: IEEE guidelines
Earn or give, but never assume, trust
Use an authentication mechanism that cannot be bypassed or tampered with
Authorize after you authenticate
Strictly separate data and control instructions, and never process control instructions received from untrusted sources
Define an approach that ensures all data are explicitly validated
Use cryptography correctly
Identify sensitive data and how they should be handled
Always consider the users
Understand how integrating external components changes your attack surface
Be flexible when considering future changes to objects and actors
See more at: https://threatpost.com/ieee-guides-software-architects-toward-secure-software-design/107965#sthash.QNrM7zZZ.dpuf

## Slide 12: Security patterns
Singleton pattern ensures that there is no spoofing of critical functions by spawning new copies
Single authenticator
Single authorizer
Use static configurations – the configuration never changes during execution

## Slide 13
http://resources.sei.cmu.edu/asset_files/TechnicalReport/2009_005_001_15110.pdf

## Slide 14: Distrustful Decomposition
The intent of the Distrustful Decomposition secure design pattern is to move separate functions into mutually untrusting programs, thereby reducing the attack surface of the individual programs that make up the system functionality and data exposed to an attacker if one of the mutually untrusting programs is compromised
This allows each program to run at lowest privilege level that fits

## Slide 15: Privilege separation
Similar to the Distrustful Decomposition
A process that has a high privilege level should adjust the privilege level of any child it forks
An initial connection before authentication should not have administrative privilege

## Slide 16: Defer to Kernel
Use existing authentication routines in the OS.
Developers don’t have to write their own authentication routines that might have holes in them.

## Slide 17: Reference monitor
Intercept all requests for resources and check their authentication.

## Slide 18: Secure Factory Design Pattern
A Factory requires a request to create an instance of a specific type and requires credentials that allow the caller to ask for that instance

## Slide 19
http://pubs.opengroup.org/onlinepubs/9299969899/toc.pdf

## Slide 20: Security requirements for vehicles
SR.1 Autonomous, strongly isolated security processing environment
SR.2 Minimal immutable trusted code to be executed prior to ECU processor
SR.3 Internal non-volatile memory for storing root security artifacts
SR.4 Non-detachable (tamper-protected) connection with ECU hardware
SR.5 Authentic, confidential, fresh comm. channel between HSM and ECU
SR.6 Autonomously controlled alert functionality (e.g., log entry, ECU halt)
SR.7 Only standardized, established security algorithms (e.g., NIST1, BSI2)

## Slide 21: Functional requirements
FR.1 Physical stress resistance to endure an automotive life-cycle of 20 years
FR.2 Bandwidth and latency performance that meets at least ISO 11898 [24]
FR.3 Compatibility with existing ECU security modules, i.e. with HIS-SHE [21]
FR.4 Compatibility with existing ECU microprocessor architectures
FR.5 Open, patent free specifications for cost-efficient OEM-wide application

## Slide 22
http://www.embedded.com/design/real-world-applications/4430395/Security-challenges-in-automotive-hardware-software-architecture-design
http://delivery.acm.org/10.1145/2490000/2485398/p458-sagstetter.pdf?ip=130.127.255.220&id=2485398&acc=ACTIVE%20SERVICE&key=A79D83B43E50B5B8.EB6DCC30042720A5.4D4702B0C3E38B35.4D4702B0C3E38B35&CFID=662283272&CFTOKEN=67633538&__acm__=1428950668_fadf7758ac684a735ba2678bc280bd21

## Slide 23
http://searchsecurity.techtarget.com/opinion/Opinion-Software-insecurity-software-flaws-in-application-architecture
https://lirias.kuleuven.be/bitstream/123456789/350066/3/paper.pdf
http://www.evita-project.org/Publications/WG11.pdf