Installing Linux with PXE and NFS

Prerequisite -
The host on which Linux is to be installed (target host) must have a NIC that supports PXE (pre-execution environment) (also known as network boot).

The server(s) -
It is necessary to have servers that provide (1) DHCP (2) TFTP and (3) NFS support. It is not necessary that all services be provided by a single server. It is necessary that the the DHCP server reside on the same LAN (broadcast domain) as the target host and that the TFTP and DHCP servers reside on the same host.

The NFS server -

This server must contain a copy of the DVD image either in normal directory based structure, or as an iso image file mounted using the loopback option.

# mount -o loop /local/jmw4/CentOS-5.3-DVD.iso /local/iso

# ls /local/iso
CentOS RELEASE-NOTES-en RELEASE-NOTES-nl
EULA RELEASE-NOTES-en.html RELEASE-NOTES-nl.html
GPL RELEASE-NOTES-en_US RELEASE-NOTES-pt_BR
images RELEASE-NOTES-en_US.html RELEASE-NOTES-pt_BR.html
isolinux RELEASE-NOTES-es RELEASE-NOTES-ro
NOTES RELEASE-NOTES-es.html RELEASE-NOTES-ro.html
RELEASE-NOTES-cs RELEASE-NOTES-fr repodata
RELEASE-NOTES-cs.html RELEASE-NOTES-fr.html RPM-GPG-KEY-beta
RELEASE-NOTES-de RELEASE-NOTES-ja RPM-GPG-KEY-CentOS-5
RELEASE-NOTES-de.html RELEASE-NOTES-ja.html TRANS.TBL

The NSF server must also contain a copy of the kickstart file to drive the installation. The directories containing these files must be exported in /etc/exports.

# cat /etc/exports
/local/jmw4 192.168.1.0/24(async,rw,no_root_squash)
/local/iso 192.168.1.0/24(async,ro,no_root_squash)

The kickstart file -

A kickstart file is generated in the root directory under the name /root/anaconda.ks.cfg during manual install. It can be used as the base for an automated install, but it is usually desirable to tailor it somewhat. Indented lines shown below must be combined with the unindented parent to create a single line in the actual kickstart.

#
# Kickstart file used in installing CentOS_64-5.3
#
install
nfs --server=192.168.70.253 --dir=/vol/vol0/CentOS_64-5.3
lang en_US.UTF-8
keyboard us
xconfig --startxonboot
network --device eth0 --bootproto static --ip 192.168.70.33
--netmask 255.255.255.0 --gateway 192.168.70.254
--nameserver 192.168.70.254
--hostname blue33.blue.cs.clemson.edu
network --device eth1 --onboot no --bootproto dhcp
--hostname blue33.blue.cs.clemson.edu
rootpw --iscrypted $1$Ong6UXgQ$8.DhusSXkXFs4y61l86Au/
firewall --disabled --port=22:tcp
authconfig --enableshadow --enablemd5
selinux --disabled
timezone --utc America/New_York
bootloader --location=mbr --driveorder=sda
--append="acpi=off rhgb quiet"
auth --useshadow --enablemd5 --enablenis --nisdomain=blue-net	--nisserver=192.168.70.254
# The following is the partition information you requested
# Note that any partitions you deleted are not expressed
# here so unless you clear all partitions first, this is
# not guaranteed to work
clearpart --linux --drives=sda
part /boot --fstype ext3 --size=100 --ondisk=sda
part pv.8 --size=0 --grow --ondisk=sda
volgroup VolGroup00 --pesize=32768 pv.8
logvol / --fstype ext3 --name=LogVol00 --vgname=VolGroup00
--size=1024 --grow
logvol swap --fstype swap --name=LogVol01 --vgname=VolGroup00
--size=1000 --grow --maxsize=1984

Following this initial section is the list of packages to be installed:

%packages
@cluster-storage
@office
@engineering-and-scientific
@mysql
@development-libs
@portuguese-support
@editors
@system-tools
@japanese-support
@british-support
@gnome-software-development

Finally some post install configuration commands may be specified to install custom files such as /etc/fstab or /etc/resolv.conf

%post
/bin/mount 192.168.70.254:/usr/local /mnt -o nolock,udp
/bin/mkdir /home2
/bin/mdkir /bluesys
/bin/cp /mnt/centos/fstab /etc/fstab
/bin/cp /mnt/centos/resolv.conf /etc/resolv.conf
# /bin/cp -rf /mnt/update/ld.so.conf.d/* /etc/ld.so.conf.d/
/bin/umount /mnt

The dhcp server -

The DHCP server configuration resides in /etc/dhcpd.conf. The following configuration can be used as a model.

ddns-update-style interim;
ignore client-updates;

The blade servers each have two NICs. We configure them with eth0 on 192.168.70.0 and eth1 on 192.168.71.0. The dhcpd daemon will not respond to requests on two different subnets unless the two subnets are defined within a shared-network container as shown here.

shared-network blue-net {
   subnet 192.168.70.0 netmask 255.255.255.0 {
        allow booting;
        allow bootp;
   # --- default gateway
        option routers 192.168.70.254;
        option subnet-mask 255.255.255.0;

        option nis-domain "blue-net";
        option domain-name "blue.cs.clemson.edu";
        option domain-name-servers 192.168.70.254;

        option time-offset -19000; # EST Time

        range dynamic-bootp 192.168.70.50 192.168.70.99;
        default-lease-time 21600;
        max-lease-time 43200;
   # Theoretically this will cause us NOT to respond to
   # broadcasts on eth1 (CCIT's LAN)
        local-address 192.168.70.254;

  # This establishes a pool of addresses that can be used for
  # truly dynamic (don't care) host addresses

        pool {
        range 192.168.70.100 192.168.70.250;
        deny known-clients;
        }

Setting up the boot loader pxelinux.0

The group container can be used to indicate the bootfile pxelinux.0 should be used for all hosts in the group. For each host, it is necessary to specify IP to MAC bindings. This setup is sometimes oxymoronically called static DHCP but it actually facilitates many aspects of blade server management.

        group {
      # tftp server address and pxe boot file
        next-server 192.168.70.254;
        filename "pxelinux.0";
        host blue26 {
        hardware ethernet 00:0D:60:9C:5A:86;
        fixed-address 192.168.70.26;
        }
        host blue28 {
        hardware ethernet 00:14:5E:3E:94:7E;
        fixed-address 192.168.70.28;
        }
        host blue29 {
        hardware ethernet 00:1A:64:F4:26:2C;
        fixed-address 192.168.70.29;
        }
        host blue30 {
        hardware ethernet 00:1A:64:F4:21:2E;
        fixed-address 192.168.70.30;
        }

        }
      }

Adding another subnet

The 192.168.71.0 subnet is defined in an analogous way. Information that was already specified for the primary subnet (routers, name-servers, etc) should not be included.

      subnet 192.168.71.0 netmask 255.255.255.0 {
        option subnet-mask 255.255.255.0;

        range dynamic-bootp 192.168.71.50 192.168.71.99;
        default-lease-time 21600;
        max-lease-time 43200;
# Theoretically this will cause us NOT to respond to
# broadcasts on eth1
        local-address 192.168.71.254;
        group {
        host blue15a {
        hardware ethernet 00:0D:60:9C:4D:23;
        fixed-address 192.168.71.15;
        }
        host blue16a {
        hardware ethernet 00:0D:60:9C:71:95;
fixed-address 192.168.71.16;
       }
        } # group
      } # subnet
   } # shared network

The tftpd server -

The tftpd server is started by xinetd. It is disabled by default. It can be enabled by using the following configuration data in the file /etc/xinetd.d/tftp

service tftp
{
        socket_type = dgram
        protocol = udp
        wait = yes
        user = root
        server = /usr/sbin/in.tftpd
        server_args = -s /tftpboot
        disable = no
        per_source = 11
        cps = 100 2
        flags = IPv4
}

As shown above the server serves files from the directory /tftpboot The tftp server serves the following data in the following order:

The pxe boot loader:
/tftboot/pxelinux.0

The boot configuration data
/tftpboot/pxelinux.cfg/C0A8461C

The install kernel and initrd files:

/tftpboot/CentOS-5.2inst.vmlinuz
/tftpboot/CentOS-5.2inst.initrd.img

Be sure that the /tftpboot directory has world rx permissions and that all subdirectories and files are likewise world readable.

The pxelinux.0 file

The file "pxelinux.0" is a binary boot loader image and it must be copied to the /tftpboot directory on the DHCP server. If you install the syslinux package on your DHCP server, then pxelinux.0 should be fround in the /usr/lib/syslinux directory.

The install kernel and initial ram disk

These files are located in the install media in the directory images/pxeboot.

[root@glint pxeboot]# pwd
/bluesys/CentOS-5.2/images/pxeboot
[root@glint pxeboot]# ls
initrd.img README TRANS.TBL vmlinuz

They must be copied to the /tftpboot directory on the tftp server. Its useful to rename them when copying so that it will be apparent from which distribution they originated:

/tftpboot/CentOS-5.2inst.vmlinuz
/tftpboot/CentOS-5.2inst.initrd.img

Boot configuration files

The boot configuration file specifies the name of the boot kernel and options that are passed to the boot kernel. These options are the same as those passed via grub and can include the name of the initial ram disk, and other parameters to be passed to the install kernel. The parameters in turn specifies the location of the kickstart file.

Individual boot configuration files live in /tftpboot/pxelinux.cfg

C0A8461C C0A8461F C0A84622 C0A84625 C0A84628 confbase genconf.c
C0A8461D C0A84620 C0A84623 C0A84626 C0A84629 default.old makeconf
C0A8461E C0A84621 C0A84624 C0A84627 C0A8462A genconf

The name of the file is the IP address of the target system in UPPER CASE HEXADECIMAL. The file associated with blue28 thus has the name C0A8461C. A file named default will be used in the absence of an IP failure to match. In addition, "wild carding" can be used as shown below. The file with the longest matching name will be used:

/tftboot/pxelinux.cfg/C000025B
/tftboot/pxelinux.cfg/C000025
/tftboot/pxelinux.cfg/C00002
/tftboot/pxelinux.cfg/C0000
/tftboot/pxelinux.cfg/C000
/tftboot/pxelinux.cfg/C00
/tftboot/pxelinux.cfg/C0
/tftboot/pxelinux.cfg/C
tftboot/pxelinux.cfg/default
The contents of the file C0A8461C used to install should be as shown (all of the parameters following APPEND must comprise a single line).

#
# This pxelinux config file can be used in an automated linux install
# The initrd and kernel are renamed versions of what is found in the
# images/pxeboot directory of the installation medium.
#
LABEL linux
KERNEL CentOS-5.2inst.vmlinuz
APPEND initrd=CentOS-5.2inst.initrd.img ksdevice=eth0	ks=nfs:192.168.70.253:/vol/vol0/blue28ks.cfg acpi=off rhgb
IPAPPEND 1

Making the process generic

If blades are configured with static IP addresses, the only host specific information in the kickstart file is:

network --device eth0 --bootproto static --ip 192.168.70.33
--netmask 255.255.255.0 --gateway 192.168.70.254
--nameserver 192.168.70.254
--hostname blue33.blue.cs.clemson.edu

Therefore, it can be convenient to create a base configuration and a script that will derive a custom config file.

#
# This pxelinux config file can be used in an automated linux install
# The initrd and kernel are renamed versions of what is found in the
# images/pxeboot directory of the installation medium.
#
LABEL linux
KERNEL CentOS-5.2inst.vmlinuz
APPEND initrd=CentOS-5.2inst.initrd.img ksdevice=eth0 ks=nfs:192.168.70.253:/vol/vol0/blue$$ks.cfg acpi=off rhgb
IPAPPEND 1

However, a better plan is to use static DHCP and avoid host specific dependencies in the the kickstart and boot files altogether. With this approach, a single boot file that uses wild carding can be used in the pxelinux.cfg directory leaving the only per host dependency is in dhcpd.conf

network --device eth0 --onboot yes --bootproto dhcp
Booting from NFS

While the procedure just described can effectively reduce the effort required to install Linux on all the blades in a cluster to simply rebooting them, its also possible to go one step further and avoid installation altogether. In this approach a host's entire filesystem is mounted on NFS. Advantages of this approach include:

- Not having to rely upon and/or replace the aging laptop type disks that were used in early blades.
- Being able to reboot and run different versions of Linux (or other operating systems) without having to re-image said aging disks.

Disadvantages may include:

- Degraded performance when many blades boot simultaneously or simultaneously attempt to load a large application.
- Excessive use of disk space on the NSF server.
- Tedious “tweaking” of filesystem contents and boot procedures to provide a truly stateless boot image (which has been done inside IBM).

1 - Create a kernel thought to be capable of root on NFS and boot it with root on the HDD. Configuration requirements include:

- In the filesystem section make sure that the NFS client is enabled and built into the kernel
- Make sure that the ethernet driver for your NIC is built into the kernel
- Make sure that CONFIG_IP_PNP, CONFIG_IP_DHCP are enabled in the networking options. These are hard to find but can be found by going to net/ipv4/Kconfig (which is where the prompt text is found along with dependencies.)
Make sure that CONFIG_ROOT_NFS is enabled in the filesystem/nfs options. The Kbuild system now has dependencies and ROOT_NFS depends on IP_PNP. Therefore it may be necessary to enable IP_PNP, save and exit, and then restart to see ROOT_NFS.

2 - After building the new kernel, copy the kernel and the initrd to the DHCP server and boot the kernel from the DHCP server with the root still on the HDD.

3 - When that is successful, use tar to create an archive containing the etc, root, sys, boot, dev, lib proc sbin tmp, var directories and
After that works tar czvf /bin /lib /var /dev /etc /root /sbin to the NFS server and boot with root on NFS.

4 - After that works, cp -a /usr to the NFS server and patch it in to fstab as a mountable file system.

5 - After that works, make a separate copy of the root components for another blade.

-